## Slide 1: Electronic Terrain and Obstacle Database
“Preparedness and Challenges”
Presented By

## Slide 2
Accuracy
Integrity / Security
DATA
End User Application
Obstacle monitoring
Macro (Satellite Image, Lidar, Drone)
Metadata
Layers
Information
Micro (Survey)
Distribution
Aeronautical Charts
AIP
Aerodrome Mapping
Obstacle
Terrain
Instrument flight procedure
Linkages of Digital Datasets
Plate 1

## Slide 3
Data to Information (Intelligent Data)
Data
Traditional Survey
Other Technologies
Location, Attribute
Paper Charts / toposheets
Vector
Raster
Spatial
Non - Spatial
Point
Line
Polygon
Z -Value
Obstacle Type
Obstacle identifier
Digital Data
Ground Control Point
Stereo Satellite Imagery, Lidar, Drone
Pixel
DEM
DTM
DSM
AIP
Automatic Generated
Schema, Metadata
Digitization , Schema
Join Attributes, Projection System, Metadata, Contour – SOI Toposheet
Manual
Format(.tiff, .Geotiff)
Integrity
Accuracy
Resolution
Vector
Raster
Format (.shp, kml .AIXM)
Plate 2

## Slide 4
Metadata
Accuracy/ (Resolution)
Traceability
Temporality
Geometry
Coverage
Reference System
Source
Format
Spatial Data
Plate 3

## Slide 5
Metadata
Plate 4

## Slide 6
Comparison of Data Formats (.shp, .kml, AIXM)
Plate 5
ICAO is recognizing AIXM (current latest version being AIXM 5.1) as a conformity mean to serve and share obstacle data (part of ETOD) with stakeholders
For the same ETOD data, SHP and kml formats may be used within a structured framework; a prerequisite being first to clearly and precisely define a conceptual data model leveraging them.
In other words, such formats are pretty useful to convey ETOD information, provided Conceptual data model, features and meta data are defined first in order to expose the obstacle data within these two formats.
AIXM on the one hand is already a structured format to receive, manage and expose ETOD data but will require specific aeronautical viewer and editor tools in order to visualize and regularly manage and maintain with temporality the data, such tool including an AIXM database capacity with import/export possibilities.
SHP and KML on the other hand are a very accessible mean and vector to share and visualize the data : SHP is standard format for Geographical Information and KML is leveraged by Google Earth.

## Slide 7
Plate 6

## Slide 8
Plate 7

## Slide 9
ACCURACY REPORT
GCP points |  |  | 
S. No. | Latitude | Longitude | Elevation ( EGM96)
26 | 28°32'43.93"N | 77°09'34.85"E | 248.809
27 | 28°32'53.18"N | 77°08'00.23"E | 249.08
28 | 28°32'20.08"N | 77°09'17.34"E | 257.911
29 | 28°31'33.98"N | 77°06'05.97"E | 237.846
30 | 28°32'05.52"N | 77°06'31.64"E | 238.121
31 | 28°30'44.67"N | 77°07'58.17"E | 273.945
Observation
The RMSE error 0.7216m is less than 1 m with acceptable limits
Plate 8

## Slide 10
Comparison between LIDAR and Satellite Photogrammetry Technologies
 | Satellite Photogrammetry | LIDAR
Data acquisition | Done via satellite by companies like Digital Globe, Airbus, ISRO. | Requires specialized and expensive equipment.
Cost | Affordable Runs in lacs for 100 sq. km | Expensive flight operation and equipment costs. Runs in Crores for 100 sq. km
Repeatability | Data can be updated as frequently as 1 week. | Prohibitively expensive to update data due to advanced flight permission and planning involved.
Accuracy | Better than 100cm | Better than 10cm
Manpower skill and software | Well developed software and workflows and enough skilled manpower available | Specialized software and skilled manpower is scarce.
Photorealistic modelling | High resolution modeling true color imaging possible | Not possible
Plate 9

## Slide 12
Plate 10

## Slide 13
Plate 11

## Slide 14
Plate 12

## Slide 15
Plate 13

## Slide 16
Plate 14

## Slide 17
Plate 15

## Slide 18
Plate 16
Obstacles Penetrating the OCS (1.2%) in Area 2b

## Slide 20
Plate 19

## Slide 21
Plate 17

## Slide 22
Plate 18

## Slide 23
Point_ID | Longitude | Latitude | Description | A= DGPS Height | B =Photogrammetry Extracted Height | Difference ( A - B)
5 | 77°08'58.85"E | 28°31'45.00"N | Top of building with Superstructure | 273.01 | 273.32 | -0.305
7 | 77°08'56.42"E | 28°31'46.02"N | Top of building | 279.11 | 278.75 | 0.360
12 | 77°08'56.96"E | 28°31'51.49"N | Top of building | 277.47 | 276.95 | 0.519
13 | 77°08'56.97"E | 28°31'51.94"N | Top of building | 271.05 | 270.57 | 0.479
14 | 77°08'57.12"E | 28°31'51.79"N | Top of building with Superstructure | 274.58 | 273.22 | 1.357*
15 | 77°08'57.73"E | 28°31'52.32"N | Top of building | 278.65 | 278.75 | -0.104
18 | 77°08'58.09"E | 28°31'52.52"N | Top of building | 278.59 | 277.85 | 0.735
20 | 77°09'06.08"E | 28°32'07.09"N | Top of building | 278.84 | 278.75 | 0.087
22 | 77°09'06.92"E | 28°32'06.65"N | Top of building with Superstructure | 281.86 | 280.85 | 1.014
24 | 77°08'30.32"E | 28°31'37.33"N | Top of building | 284.41 | 284.37 | 0.039
27 | 77°08'27.31"E | 28°31'34.87"N | Top of building | 283.52 | 283.38 | 0.139
28 | 77°08'27.31"E | 28°31'34.87"N | Top of building with Superstructure | 285.38 | 285.88 | -0.502
30 | 77°08'09.98"E | 28°31'38.34"N | Top of building | 279.28 | 279.38 | -0.100
31 | 77°08'09.96"E | 28°31'38.55"N | Top of building with Superstructure | 282.39 | 281.76 | 0.630
34 | 77°08'11.12"E | 28°31'38.65"N | Top of building | 282.72 | 282.51 | 0.212
Validation of obstacle height (AMSL, meter) extracted through photogrammetry with field Survey
Calculated vertical accuracy report based on Top elevation:
Root Mean Square Error (RMSE):
Z- Value absolute RMSE = √((-0.305)2 + (0.360)2+ (0.305)2+ (-0.519)2+ (0.479)2+ (1.357)2 + (-0.104)2+ (0.735)2+ (0.087)2+ (1.014)2+ (0.039)2+ (0.139)2 + (-0.502)2+ (-0.100)2+ (0.630)2 + (0.212)2)/15
= √(0.32376 )/15
= +/- 0.569 m < 1 m
It is Observed that absolute RMSE < 1 m, Which is acceptable as per accuracy certain define for Area 2.
*Maximum difference of absolute Z- Value: 1.35 m but this is an aberration and needs to be checked again.
Plate 20